## Slide 1: VA8801 SDK Handbook V3.2

## Slide 2: Outline
VA8801 AI Chip Introduction
VA8801 Development Preparation
VA8801 Projects and AI Tool Introduction
VA8801 Firmware Update and AI Model Validation Introduction

## Slide 3: Outline – VA8801 AI Chip Introduction
Architecture Introduction
SDK Directory Introduction
AI Model Zoo Introduction
Architecture Introduction
SDK Directory Introduction
AI Model Zoo Introduction
Starting

## Slide 4: Outline – VA8801 Development Preparation
How to Bring Up DemoKit Board
How to Install Development Environment
How to Start Development
Bring Up DemoKit Board
Starting
Install Development Environment
(VSCode+EIDE)
Starting VA8801 Development

## Slide 5: Outline – VA8801 Projects and Tools Introduction
SDK TinyML Project Brief
SDK NPU Project Brief
How to Using Tengen Compiler (AI Model Compiler)
TinyML Project Brief
NPU
Project Brief
Tengen Compiler Introduction
Starting

## Slide 6: Outline – VA8801 Firmware Update and AI Model Validation Introduction
How to Update VA8801 Firmware via DFU(Device Firmware Update) Tool
How to Validation AI Model(.tflite int8) on VA8801 chip via DUT(Device Under Test) tool
DFU Tool
Update VA8801 Firmware
Starting
DUT Tool
Validation TFLite INT8
Model on Chip

## Slide 7: VA8801 AI Chip Introduction

## Slide 8: VA8801 Architecture Introduction – 1
TinyML
Project
Tengen Compiler
And
NPU Project
CPU(System)
NPU(AI)
VA8801 AI Chip

## Slide 9: VA8801 Architecture Introduction – 2
TinyML Project
  VA8801 BSP/SDK Switch Target - Dual_AV(audio+video) , Face_detection , Gesture
  The above Targets have corresponding Targets in NPU Project
    if the [TinyML project chooses: Gesture], the [NPU Project Target also chooses: Gesture]
NPU Project
  VA8801 AI Mode Zoo
    https://github.com/FITI-HCITA/VA8801_Model_Zoo
    git clone https://github.com/FITI-HCITA/VA8801_Model_Zoo.git
  Self-develop AI Model
    Support OPs, please refer to DLA Docs SDK root path\ VA8801_BSPSDK_v3.000.000\Doc\DLA\VA8801_DLA_Guide_V0.3_20240521.pdf)
    If using PyTorch to train the AI model, you need to export it in .onnx format  convert to TensorFlow  Quantize INT8(Full integer quantization) INT8 AI model (.tflite)
    If using TensorFlow to train the AI model  Quantize INT8(Full integer quantization)  INT8 AI model (.tflite)
  The current Tengen Compiler supports only TFLite INT8
    Generate AI Model C Code in your specified INT8 AI model (.tflite) path
  Copy Model C code to SDK NPU Project
    Reference SDK root path\VA8801_BSPSDK_v3.000.000\Tengen Compiler\Tengen Compiler User Guide v1.0.3.pdf
  NPU Switch Target
    If the NPU project chooses Gesture, the TinyML Project Target also chooses Gesture
    if self-develop AI Model , you can reference Gesture Target then modify meet your app (ref page Self-develop AI Model – How to Modify SDK Project)
  Development pre/post process
    Self-define development pre/post process in SDK NPU Project main_and_config folder
    Reference SDK root path\VA8801_BSPSDK_v3.000.000\Doc\VSCode\ VSCode_Toolchain_Build System_user guide_v2.0.pdf

## Slide 10: VA8801 Architecture Introduction – 3
DFU(Device Firmware Update) Tool
  Reference SDK root path\VA8801_BSPSDK_v3.000.000\DFU Tool\ FITI_VA8801_DFU_ToolKit_v1.0.0.pdf
Demo Tool
  Reference SDK root path\VA8801_BSPSDK_v3.000.000\Demo Tool\ VA8801_Demo_Tool_UserGuide_V0.1_20240305.pdf
Others tool - DUT(Device Under Test) tool
  The Device Under Test (DUT) tool provides user-fed image data from a PC or notebook, then validates the AI model(.tflite INT8)
  Reference SDK root path\VA8801_BSPSDK_v3.000.000\DUT Tool\ VA8801_DUT_Guide_V1.0.pdf
Notes. The AI model and image data share DDR memory. The memory layout can be referenced as follows:
AI Model
C Code
Usage Space
AI Model
Input Image data
Usage Space
DDR_16M Memory Layout
0x80000000
0x81000000
AI Model
C Code
Usage Space
(15.7MB)
Image data
(320x320x3)
(size:0.3M)
DDR use example:
0x80000000
0x81000000
0x80FB5000
0x80FB4FFC

## Slide 11: VA8801 SDK Directory Introduction – 1
Folder | Description
AI Models | Fitipower AI Model ModeCard A+V : Abnormal sound + Human detection Face_detection Gesture https://github.com/FITI-HCITA/VA8801_Model_Zoo
BSP | VA8801 BSP introduction
Code | VA8801 SDK Source code
Demo Tool | Display the result image after AI inference. Ex. Detect a human face and enclose it with a bounding box.
DFU Tool | Device Firmware Update(DFU) tool via USB update VA8801 firmware
Doc | VA8801 Video CDM_ROI User guide VA8801 Datasheet Tengen DLA doc SDK SW API comment doc VSCode for Development VA8801 IDE

## Slide 12: VA8801 SDK Directory Introduction – 2
Folder | Description
Download Tool | Generate VA8801 Output binary file Update VA8801 Firmware
Driver | DediProg SF600Plus_Driver for VA8801 FW update, If you have an SF600 Plus device WinUSB_Driver for VA8801 USB transfer image PC_UART_Drivers for print VA8801 log message
DUT Tool | The Device Under Test (DUT) tool provides user-fed image data from a PC or notebook, then validates the AI model
DVK | VA8801 Demo Kit Schematic
NPU Bin | Fitipower AI Model zoo binary file
Tengen Compiler | Use the Fitipower AI Compiler to compile the AI model into C code

## Slide 13: VA8801 Development Preparation

## Slide 14: VA8801 AI Model Zoo Introduction
We provide a series of pre-trained models for different application scenarios for you to use, with Fitipower VA8801 SDK, you can test or inference on these models and easily deploy them to VA8801 device
VA8801 Model Zoo focuses on providing models trained on VA8801 optimized neural networks, which are tailored to real-world application scenarios and enable faster and more accurate inference on VA8801 device. We will provide more models later
VA8801 AI Model Zoo github link
  https://github.com/FITI-HCITA/VA8801_Model_Zoo

## Slide 15: How to Bring Up DemoKit Board – 1
The default firmware for the VA8801 DemoKit is Dual_A_V
  Audio – abnormal sound recognize(such as baby crying)
  Video – Human detection
Power supply
  Micro USB connect to PC/NB
  Adapter - output 5V
Use the Demo Tool to display images and human detection results
Demo Tool :

## Slide 16: How to Bring Up DemoKit Board – 2
Power supply: Micro USB connect to PC/NB
Button:
*push up – power on
VA8801 Demo kit board

## Slide 17: How to Bring Up DemoKit Board – 3
UART1
UART0
Pin from top to bottom:
P1.UART_RX
P3.UART_TX
P5.UART_GND
FT232 connect to PC/NB
FT232_RX connect to UART_TX
FT232_TX connect to UART_RX
FT232_GND connect to UART_GND
Micro USB connect to PC/NB
Push button to power on
VA8801 Demo kit board

## Slide 18: How to Bring Up DemoKit Board – 4
Step 1. Click on "Search"
Step 2. Choose the COM port; you can check in Device Manager under "Ports (COM & LPT)" to find the COM port associated with a USB serial device
Step 3. Switch to the "Image" page
1.
2.
3.
4.
5.
Demo Tool
2.
6.
*The first time you use it, after VA8801 is powered on, you need to install the WinUSB Driver.
(SDK root path\VA8801_BSPSDK_v3.000.000\Driver\WinUSB_Driver.7z)

## Slide 19: How to Bring Up DemoKit Board – 5
Step 3. Switch to the "Image" page
Step 4. Click "Connect"
Step 5.
Tick User Def
Face Detection, Gesture - RGB888 W:320 H:320
A+V - Y8 W:96 H:96
Push enter after input W and H (red text will turn black)
Face Detection, Gesture - Tick RB ch
Tick +128
Tick AI info - Enable AI info (bounding box)
Step 6. Click "Write"
1.
2.
3.
4.
6.
Demo Tool
5.

## Slide 20: How to Bring Up DemoKit Board – 6
Human detection + Abnormal sound recognize result
Description
When abnormal sound is detected, the output will be the display abnormal sound (such as baby crying)
Using NB or smartphone ..etc play folder [Abnormal Sound file\Baby_cry.wav]
UART0 System log
UART1 NPU log

## Slide 21: How to Install Development Environment
Install Visual Studio Code(VSCode)
  https://code.visualstudio.com/download
Install Embedded IDE(EIDE) plug in VSCode
  https://marketplace.visualstudio.com/items?itemName=CL.eide
Install .NET6 X64 Runtime package
  After install EIDE done, The plug-in will auto download and install eide-binaries and .NET6 X64 Runtime package
Install GNU Arm Embedded Toolchain in VSCode
Detail reference :
SDK root path\VA8801_BSPSDK_V3.000.000_release\Doc\VSCode\VSCode_Toolchain_Build System_user guide_v2.0.pdf

## Slide 22: How to Start Development
Let’s
Start
Bring up VA8801 DVK
Install WinUSB driver
Install UART driver
Build TinyML Project
Build NPU Project
DFU Tool
Choose SYS.bin +
NPU_code.bin + NPU_data.bin
then Burn to VA8801
Demo Tool: Display image and ai model post process result(NMS)
DUT Tool: user-fed image data from a PC/NB validates AI model(.tflite INT8)
Terminal: UART1 Print AI Inference result log message
Install VSCode Development Kit
git clone VA8801
Model Zoo
Tengen Compiler
Generate Model C code

## Slide 23: VA8801 Projects and AI Tool Introduction

## Slide 24: VA8801 Projects and AI Tool Introduction
The VA8801 SDK project is divided into CPU(System) and NPU(AI) projects, each with its corresponding Target
TinyML Project
Choose Target
Dual_A_V
NPU Project
Choose Target
Dual_AV
CPU(System)
NPU(AI)
TinyML Project
Choose Target
Face_Detection
NPU Project
Choose Target
Face_Detection
CPU(System)
NPU(AI)
TinyML Project
Choose Target
Gesture
NPU Project
Choose Target
Gesture
CPU(System)
NPU(AI)

## Slide 25: VA8801 TinyML Project Brief – 1
Project Resources
  Display project source code folder, builder output files
Chip Support Package
  Ignore
Builder Configuration
  Setting CPU Type, Linker Script(.ld), Complier/Linker configuration etc..
Flasher Configuration
  Setting Debug mode configuration
Project Attributes
  Setting Project Include header file paths, Preprocessor Defines, Library Search Directories etc..
Project Setting
  Setting Project Name, Output Folder Name, Environment Variables
Build
Clean
Program Flash
Rebuild
EIDE Project
Project Activated
Project Deactivated
Project Status

## Slide 26: VA8801 TinyML Project Brief – 2
You can develop your application in task_host.c
For example, AI inference results can be transmitted to applications, such as the main board SOC(or MCU), through peripheral interfaces like I2C or UART

## Slide 27: VA8801 NPU Project Brief
Project Resources
  Display project source code folder, builder output files
  Tengen Compiler output file(AI Model C code)
Chip Support Package
  Ignore
Builder Configuration
  Setting CPU Type, Linker Script(.ld), Complier/Linker configuration etc..
Flasher Configuration
  Setting Debug mode configuration
Project Attributes
  Setting Project Include header file paths, Preprocessor Defines, Library Search Directories etc..
Project Setting
  Setting Project Name, Output Folder Name, Environment Variables
Build
Clean
Program Flash
Rebuild
EIDE Project
Project Activated
Project Deactivated
Project Status

## Slide 28: How to Using Tengen Compiler – 1
Prerequisites
  Window OS and install Docker Desktop and WSL2 on Windows
  At least free memory space 3.5GB
  Tengen Compiler image: tengen_v1.1.2.tar
Purpose
  Compile the AI model into C code, then use the VA8801 SDK NPU project to compile the AI model C code into binary files, and deploy them to the VA8801 chip
Current version Limitations
  Support TensorFlow Lite and quantized to int8 model only
  Support OPs, please refer to DLA Docs SDK root path\ VA8801_BSPSDK_v3.000.001\Doc\DLA\VA8801_DLA_Guide_V0.3_20240521.pdf)
AI Model Size Limitations
  The AI model shares DDR memory with image data, and the DDR memory size is 16MB.
  For example, if the resolution of the image data for the model is 320x320x3(about 0.3MB), the size of the AI model should be approximately less than 15.7MB
Detail reference SDK root path\VA8801_BSPSDK_V3.000.001_release\Tengen Compiler\Tengen Compiler User Guide v1.0.3.pdf

## Slide 29: How to Using Tengen Compiler – 2
Open docker desktop ap after docker install done
Open terminal(ex. PowerShell) then Point the path to the directory location of Tengen
Docker command to load image from tar file(file name reference SDK root path\ VA8801_BSPSDK_v3.000.000\ Tengen Compiler\tengen_vx.x.x.tar )
  EX: docker load --input tengen_v1.1.0.tar
Docker command to check images
  EX: docker image ls

## Slide 30: How to Using Tengen Compiler – 3
You can also see the image at docker desktop

## Slide 31: How to Using Tengen Compiler – 4
Example Docker command :
  docker run -v D:\VA8801_Documnet_SDK\tmp_sdk3.0\VA8801_BSPSDK_v3.000.000\Model_zoo\VA8801_Model_Zoo\ObjectDetection\Hand_Gestures:/volume tengen:1.1.0 ./tengen --dla_version 3.7.4 --compile_mode 1 --model_path volume/Hand_Gestures_3_001_001.tflite --output_folder /volume
Green : Enter your ai model local path
Yellow : Enter Tengen version. The Tengen version, you can navigate to the SDK root path: \VA8801_BSPSDK_V3.000.001_release\Tengen Compiler\tanger_vx.x.x
Purple : Enter your Model name
Docker command to run Tengen service:
docker run -v $Folder:/volume tengen:1.1.2 ./tengen --dla_version $DLA_VERSION --compile_mode $MODE --model_path volume/$FILE –name default1 --output_folder /volume
Parameters:
-$FOLDER: The folder model located:
-$FILE: The model file name
-$DLA_VERSION: Support: 3.7.4, 3.9.2, latest
-$MODE: 0: Pure C Codegen, 1: Dual DLA (Suggested options), 2: Single DLA
Then, you can find output folder at your $FOLDER, the name will be model_$FILE

## Slide 32: How to Using Tengen Compiler – 5
Model codegen done

## Slide 33: VA8801 Firmware Update and AI Model Validation Introduction

## Slide 34: How to Update VA8801 Firmware via DFU(Device Firmware Update) Tool – 1
For the first use, you need to update the VA8801 Second Bootloader firmware
  Prepare a UART to USB adapter (e.g., FT232) for the hardware
  VA8801 DVK HW UART3 Setup and FT232 connect to PC/NB

## Slide 35: How to Update VA8801 Firmware via DFU(Device Firmware Update) Tool – 2
For the first use, you need to update the VA8801 Second Bootloader firmware
  Prepare a UART to USB adapter (e.g., FT232) for the hardware
  Connect the DuPont line from VA8801 DVK HW JPIO_7_Pin1 (near the arrow) to JVH_VDD33 to pull it high
JPIO_7_Pin1
*If there is a jumper, please remove it.
JVH_VDD33

## Slide 36: How to Update VA8801 Firmware via DFU(Device Firmware Update) Tool – 3
For the first use, you need to update the VA8801 Second Bootloader firmware
  Prepare a UART to USB adapter (e.g., FT232) for the hardware
  VA8801 Flash Button setup – Middle Button Push Down , Right/Left Push Up
Up Down Up
Reset button
GND

## Slide 37: How to Update VA8801 Firmware via DFU(Device Firmware Update) Tool – 4
Use the DUT Tool to update the second bootloader firmware via UART3
  Search UART3 the COM port; you can check in Device Manager under "Ports (COM & LPT)" to find the COM port
  Baud rate 460800
  Click Connect
  Click VA8801 DVK Reset Button
  Display [Info] Start Download Flash
  Header log message
  HW setup: VA8801 DVK Flash Button setup –
  All button Push Up
  Click 2nd Boot diagram upgrade the VA8801
  Second Bootloader firmware
  VA8801 Second Bootloader Update done
  HW setup: Click VA8801 Reset Button
Second Bootloader update done.

## Slide 38: How to Update VA8801 Firmware via DFU(Device Firmware Update) Tool – 5
Use zadig.exe to install the FITI DFU Tool driver. The path to zadig.exe is in the SDK root path\VA8801_BSPSDK_v3.000.000\DFU Tool
Select Options  List All Devices
Select libusb-win32(v1.2.6.0)
Click Install Driver

## Slide 39: How to Update VA8801 Firmware via DFU(Device Firmware Update) Tool – 6
Now, close and reopen the DFU Tool, then you can use the DUT Tool to update the VA88001 firmware
The wiring of VA8801 DVK UART3 can be removed
Click on the folder icon and select the binary file
Custom Code ST Addr: TinyML
NPU0 Code ST Addr: NPU_code.bin
NPU1 Code ST Addr: NPU_data.bin
Update the firmware sequentially following the black arrow symbols

## Slide 40: How to Update VA8801 Firmware via DFU(Device Firmware Update) Tool – 7
When VA8801 DVK FW update done, VA8801 DVK HW JPIO_7_Pin1 (near the arrow) to GND
System run After Click VA8801 DVK Reset button
  You can check if the system is working properly through the terminal(ex. Tera Term) log
Detail operation reference VA8801_DUF_Tool_User_Guide.mp4
Detail Reference SDK root path\VA8801_BSPSDK_v3.000.000\DFU Tool\FITI_VA8801_DFU_ToolKit_v1.0.0.pdf
Note1. The second bootloader only needs to be updated once
Note2. If you need to update the VA8801 firmware again, you should pull JPIO_7_Pin1 high. After updating the firmware done, pull it low

## Slide 41: How to Validation AI Model on VA8801 chip via DUT(Device Under Test) Tool – 1
DUT Tool
Fed-image
AI Inference
on VA8801 chip
Generate
AI Inference
Results(NMS)
PC/NB
AI Inference Simulation results
TFLite INT8(.tflite) Model Validation
Generate
AI Inference
Results(NMS)
Compare Model
post process
Results(NMS)
Test
Dataset
Detail Reference SDK root path\VA8801_BSPSDK_v3.000.000\DUT Tool\VA8801_DUT_Guide_V1.0.pdf

## Slide 42: How to Validation AI Model on VA8801 chip via DUT(Device Under Test) Tool – 2
Switch 「Image verify」 page
Choose input image format
Enter SOC_ISP_AXI_ADDR , in va8801_bsp\VA8801\PERIPHERALS\Drivers\inc\SOC_ISP_Driver.h
Enter input image height, width
Choose 「 APP4 」
Choose input image in DUT Tool root path, file name fixed 1.bmp or 1.jpg
Click Auto Img
2.
3.
4.
5.
6.
7.
1.
Detail Reference SDK root path\VA8801_BSPSDK_v3.000.000\DUT Tool\VA8801_DUT_Guide_V1.0.pdf
DUT Tool

## Slide 43: Appendix

## Slide 44: Self-develop AI Model – How to Modify SDK Project 1
If you are developing your own AI model in TinyML and NPU projects, it is recommended to choose Gesture as the target for code-based modifications. The areas that need to be modified are as follows
  TinyML Project
    Modify SOC_ISP_AXI_ADDR address in va8801_bsp\VA8801\PERIPHERALS\Drivers\inc\SOC_ISP_Driver.h
    For example: AI Model input image : 320x320x3, SOC_ISP_AXI_ADDR = 0x81000000 – 0x4B000 = 0x80FB5000
    SOC_ISP_AXI_ADDR need setting 0x88FB5000
    2. Modify the input image resolution according to the AI model in va8801_bsp\VA8801\PERIPHERALS\BSP\Components\inc\fiti_camera.h
AI Model
C Code
Usage Space
AI Model
Input Image data
Usage Space
DDR_16M Memory Layout
0x80000000
0x81000000
TinyML Project
Choose Target
Gesture
NPU Project
Choose Target
Gesture
CPU(System)
NPU(AI)

## Slide 45: Self-develop AI Model – How to Modify SDK Project 2
If you are developing your own AI model in TinyML and NPU projects, it is recommended to choose Gesture as the target for code-based modifications. The areas that need to be modified are as follows
  NPU Project
    Model head file name in app\task_nup_gesture.c
    Model API function name in app\task_nup_gesture.c
    Model struct name in app\task_nup_gesture.c
    Pre/post process in main_and_config\pre_pocess.c、 post_pocess.c
    Modify the image input resolution in NPU\Project\NPU\dla.h, which will be referenced in the post_process.c

## Slide 46: Self-develop AI Model – How to Modify SDK Project 2
Modify the name in the red box .
referenced in the "tvmgen_model_xxx.h" file in the include folder of the AI Model C code generated by the Tengen compiler.
2.
1.
3.
4.
5.
6.
7.
8.

## Slide 47: Self-develop AI Model – How to Modify SDK Project 3
2.
3.
1.
4.
5.
The naming of 1 to 8 will be based on the AI Model
7.
6.
8.

## Slide 48: Self-develop AI Model – How to Modify SDK Project 4
va8801_bsp\VA8801\NPU\Project\NPU\dla.h
  Modify this section of the code according to the AI model

## Slide 49: REVISION HISTORY – 1
Revision | Date | Author | Description
3.0 | 2024/05/27 | Jason SYU | New issued
3.1 | 2024/05/30 | Jason SYU | Modify How to Start VA8801 Flow chart Update Self-develop AI Model – How to Modify Target in NPU Project Update VA8801 AI Model zoo Introduction Update How to Update VA8801 Firmware via DFU(Device Firmware Update) Tool
3.2 | 2024/06/07 | Jason SYU | Modify the Outline struct Update How to Update VA8801 Firmware via DFU(Device Firmware Update) Tool – 2 ~ 7 Update How to Start Development flow chart Update How to Using Tengen Compiler – 2 ~ 5 Update How to Validation AI Model on VA8801 chip via DUT(Device Under Test) Tool – 1 ~2 Update Self-develop AI Model – How to Modify SDK Project

## Slide 50
THANKS